## Slide 1: Find your hidden factory in 30 days
A FIELD GUIDE FOR PLANT AND FINANCE TEAMS
A 7-step method to put a price tag on every production loss and recover output from the equipment you already have.
7 steps
4 weeks
One loss Pareto in €

## Slide 2: Your team talks in minutes. Your CFO decides in euros.
WHY THIS MATTERS
When improvement results never reach the financial statements, support fades. The losses stay.
≈60%
OEE in an average plant
≈85%
world class for discrete lines
THE PRINCIPLE
If a loss has no price tag, it has no priority.

## Slide 3: Measure true OEE with three numbers
WEEK 1 · STEP 1
Scheduled time, good units and the ideal rate. Nothing else.
OEE =
(good units ÷ ideal rate)
÷ scheduled time
Example: 4,362 good units ÷ 4 per minute = 1,090 minutes of perfect production, in 1,830 scheduled minutes.
OEE 59.6%
No ideal rate? Use the best 4 hours of your last 400. Method and example: R.C. Hansen, Overall Equipment Effectiveness.

## Slide 4: Classify every minute. No “other”.
WEEK 1 · STEP 2
A minute with no reason can’t be priced, and a loss with no price won’t be fixed.
Chart: Where scheduled time goes (Hansen’s 40-hour example)
| Scheduled time
OEE 59.6% | 59.6
Downtime 14.2% | 14.2
Speed loss 9.3% | 9.3
Planned stops 9.3% | 9.3
Scrap 4.3% | 4.3
Induced stops 3.3% | 3.3
The check: OEE plus every loss must add up to 100% of scheduled time. If it doesn’t, a loss is hiding.

## Slide 5: Start at the bottleneck
WEEK 1 · STEP 3
A minute lost at the bottleneck is a minute lost for the whole plant. A minute lost elsewhere may cost nothing.
Filling
140/min
→
Capping
100/min
→
Packing
160/min
Sample line: capping sets the pace for all three steps
Ask before every project: if this step gets better, will plant output or profit move? If not, work somewhere else.

## Slide 6: Put a price tag on every loss
WEEK 2 · STEP 4
You only need your selling price and gross margin per product.
Revenue at risk
lost units × selling price
€48.00 / min
Profit impact
lost units × gross margin
€15.36 / min
Cost of downtime
labour and overheads while you wait
€2.47 / min
Sample data: 20 units a minute, €2.40 per unit, 32% margin, €148 an hour labour and overheads = €1,070 per hour stopped. Price your own line →

## Slide 7: Rank by money, not minutes
WEEK 2 · STEP 5
Slow running rarely makes the morning meeting. Priced per year, it often beats the stop everyone remembers.
Chart: Profit impact per year
| Scrap: label defects | Changeover overruns | Unplanned stop: filler jams | Slow running after restarts
Profit impact per year (€) | 33178 | 102682 | 154022 | 165888
Sample data from the loss price tag calculator. Ranked by minutes stopped, filler jams would have looked like the priority.

## Slide 8: Pick no more than three losses
WEEK 3 · STEP 6
Finish them fast. Each one gets the same four parts.
Evidence
Stop codes, operator notes, the timeline
Step 1
Owner
One name, not a department
Step 2
Action
A countermeasure: work order, SOP update, training
Step 3
Verified result
Checked against production data
Done
Look for the cause in the process, not the person. Problems usually sit in the system.

## Slide 9: A fix counts when output moves
WEEK 4 · STEP 7
Not when the task is closed. Compare the loss before and after, in units and in euros.
P
Plan the change
D
Do it on the line
C
Check with production data
A
Make it the standard
Can you sell the extra output? Then the gain is profit.
Can’t you? It comes back as shorter shifts and less overtime.
Then go back to step 1 with the next loss.

## Slide 10: Find the money first. Then fix it.
YOUR 30-DAY CHECKLIST
Week 1: true OEE on the bottleneck, every minute classified
Week 2: a price tag on each loss, ranked in euros
Week 3: top three losses, each with an owner and an action
Week 4: results verified with production data, reported in euros
Price one minute on your line
Free loss price tag calculator, 3 minutes
Open →
Book a 30-minute demo with your own line →